## Slide 1: Air Bearing Auto-Balancer
Dmitriy Rivkin

## Slide 2: Objective
Automated balancing of air bearing with minimal human involvement
  Balancing means center of gravity is co-located with center of rotation, eliminating torque due to gravity

## Slide 3: Basics
Balancing is achieved using three linearly translating motorized masses
Notes: Kim and Agrawal

## Slide 4: Basics
Balancing happens offline
  Weights not being adjusted during sat testing
Coarse adjustments are manual
  Allows smaller sliding weights, increased precision, relaxed requirement on actuators
Battery powered

## Slide 5: Sensors
IMU
  Gravity vector
  Rotation rates
Inclinometers
  Can give better gravity vector than IMU

## Slide 6: Actuators
Desirable traits
  High force
  High detent force (when turned off)
  Low magnetic interference
  High precision
  High accuracy

## Slide 7: Actuators
Piezo Motors > Electromagnetic Motors
  Better in all respects mentioned above
  Simpler (less moving parts)
But:
  Potentially more costly
  Smaller displacement
  Complicated to drive

## Slide 8: Proposed Actuator 1
PI N-422
7N push force
10N hold force
35mm travel
  I think this can be increased
No encoder (add later if needed)
4 N/um stiffness

## Slide 9: Proposed Actuator 1
100g, 4 channel driver available for the N-422
Cost:
  $772 per actuator
  $1101 for the driver
Lead time: 4 – 5 weeks

## Slide 10: Proposed Actuator 2
A stepper motor turns a lead screw with an anti-backlash nut on it
Notes: Photo cred: nook industries

## Slide 11: Proposed Actuator 2
Advantages:
  High force
  Large travel
  Low cost
  Short lead time
Disadvantages:
  Lower resolution
  Potentially lower “stiffness”
  Permanent magnets in stepper motor may affect performance of magnetometers on test bed

## Slide 12: Balancing Approaches
Most rely on spinning the test-bed and measuring rotational rates
Can be grouped into batch estimation type solutions and feedback solutions

## Slide 13: Side By Side Comparison of Actuators 1 and 2

## Slide 14: Balancing Approaches
Batch estimation (Li and Gao, Chesi and Gong)
  Develop equations of motion
  Actuate system (with reaction wheels)
  Use some (least squares) approach to find best estimate of CoG
  Once CoG is known, move masses to compensate
  Sensitive to knowledge of actuator parameters
  Need to know MOI (or estimate it at the same time)
  Multiple iterations needed
  Requires actuation

## Slide 15: Balancing Approaches
Alternative Approach to Batch Estimation
  Move masses
  Measure change of equilibrium position
  Compute center of mass
  Move masses to compensate

## Slide 16: Balancing Approaches
Feedback approach (Kim and Agrawal, Chesi and Gong)
  Actuate system
  While system is spinning, apply feedback control law to drive external torque to zero
  Requires knowledge of initial MOI
  Requires IMU
  Requires actuation

## Slide 17: My Proposed Approach
Step 1: Move CoG to Z axis using gravity vector feedback
  Move around the weights until the bearing sits flat, but is still bottom heavy

## Slide 18: My Proposed Approach
Step 2: Tilt the air bearing and rest it on a force guage. Slide up z axis mass until force guage reads zero.
  Force on the guage is proportional to the torque being applied by gravity
  Z axis actuator must be directly below CoR

## Slide 19: Benefits of My Approach
No need to know MOI
  Important since we plan on switching test-beds a lot
No need for accurate knowledge of actuator position
Not sensitive to x and y axis actuator alignment
Computationally non-intensive

## Slide 20: Plan
Hardware is pretty much the same for all of the possible approaches
Step 1: Build the rig well
  My method shouldn’t be very sensitive to the precision of the build, but others may be
Step 2: Implement my method using IMU for gravity vector
Step 3: If it doesn’t work, we try something that’s been published (hardware is already set up)

## Slide 21: Build Plan
See SolidWorks mock up

## Slide 22: Keep in Mind
No mass motions
  Rigid platform
  All components well secured
  Wires
Precise placement of actuators (especially z axis) and sensors is highly desirable
  Use quality machining

## Slide 23: Some References
Chesi et al. “Automatic Mass Balancing of a Spacecraft Three-Axis Simulator: Analysis and Experimentation.” 2014
Kim, J.J. and Agrawal, B.N. “Automatic Mass Balancing of Air-Bearing-Based Three-Axis Rotational Spacecraft Simulator.” 2009.
Meissner, D.M. Thesis. 2009. Naval Postgraduate School.
Li, Y. and Gao,Y. “Equations of Motion for the Automatic Balancing System of 3-DOF Spacecraft Attitude Control Simulator”.
Smith, G.A. “Dynamic Simulators for Test of Space Vehicle Attitude Control Systems.”1964.